## Slide 1: NextGen Simulation Development Tools: ngen-datastream
Lynker: Jordan laser, Zach wills, Mike Johnson, Justin Singh-Mohudpur, Nels frazier, Austin Raney
Alabama Water Institute: Arpita patel, James Halgren, Josh Cunningham, Shahabul alam, trupesh patel, hari teja jajula, Benjamin Lee
SPRING 2024

## Slide 2
Motivation
Development Roadmap
Conceptual model
Usage
Research Datastream
Workshop
Future work
Overview

## Slide 3: motivation
Uniform data pipeline that abstracts the laborious process of collecting input data and executing NextGen
Reproducibility
Need baseline NextGen dataset to evaluate new realizations against
Scaling from laptop to HPC
  ngen-datasteam will perform every step in executing NextGen. The user can compute steps separately and provide those files directly.
  *Batteries included while not dogmatic*
  Enforces the NextGen In A Box standard run directory.
  Metadata – all relevant information about user inputs, code versions, host architecture, etc. so that a NextGen execution can be understood and reproduced.
  ngen-datastream can issue NextGen jobs to an AWS state machine that use Lambda functions to coordinate NextGen executions in the cloud. This infrastructure is behind the NextGen research datastream. In addition, allows users to customize their host to match their compute requirements.

## Slide 4: Development roadmap
Planning
Identifying needs in community
Software architecture decisions
Development
Writing the software
Developer based testing
Deployment
Releasing software to community
ngen-datastream version 1.0
Testing
Continuous Integration Continuous Deployment (CI/CD)
Feedback from community
Maintenance
Add features
ngen-datastream is already a powerful tool, but is still under development and has not been rigorously tested within the community
We encourage community feedback and questions. If you discover a bug, or would appreciate different functionality, let us know by submitting an issue to the repository
We are here!

## Slide 5
ngen-datastream refers to the software chain that builds and validates NextGen input packages (ngen-run/), executes NextGen through NextGen In A Box (NGIAB), and versions the entire run for reproducibility.
Validation
NGEN-DATASTREAM
Prepare configuration and data inputs
1
2
3
Versioning
4
This enforces a standard folder ngen-run/ which makes validation and versioning possible. A standard run folder also allows for other new tools to easily integrate with NGIAB (e.g., DataPreprocessor).

## Slide 6
Hydrofabric
Defines spatial domain
Weights
Indices and coverage used to extract catchment averaged forcings
Forcings
NEXTGEN BMI model configuration
Performs conversion between National Water Model and NextGen forcings formats
Required files for NextGen BMI modules
GET
CALC
CALC
CALC
Prepare configuration and data inputs
1
Required steps to build ngen-run/config and ngen-run/forcings

## Slide 7
https://www.lynker-spatial.com/#hydrofabric/v20.1/gpkg/
Hydrofabric
Defines spatial domain
GET
Prepare configuration and data inputs
1

## Slide 8
“What if I want to define my own spatial domain?”
Do you know the catchment id you want to subset with?
Use the subsetting options!
hfsubset is integrated into ngen-datastream
Hydrofabric
Defines spatial domain
GET
Prepare configuration and data inputs
1

## Slide 9
Hydrofabric
Defines spatial domain
Weights
Indices and coverage used to extract catchment averaged forcings
Forcings
NEXTGEN BMI model configuration
Performs conversion between National Water Model and NextGen forcings formats
Required files for NextGen BMI modules
GET
CALC
CALC
CALC
Prepare configuration and data inputs
1
Required steps to build ngen-run/config and ngen-run/forcings

## Slide 10
Index: 27461
Coverage: 25%
Index: 27463
Coverage: 75%
NWM
NGEN
Hydrofabric
Defines spatial domain
Weights
Indices and coverage used to extract catchment averaged forcings
GET
CALC
Prepare configuration and data inputs
1

## Slide 11
Hydrofabric
Defines spatial domain
Weights
Indices and coverage used to extract catchment averaged forcings
Forcings
Performs conversion between National Water Model and NextGen forcings formats
GET
CALC
CALC
Prepare configuration and data inputs
1

## Slide 12
Hydrofabric
Defines spatial domain
Weights
Indices and coverage used to extract catchment averaged forcings
Forcings
NEXTGEN BMI model configuration
Performs conversion between National Water Model and NextGen forcings formats
Required files for NextGen BMI modules
GET
CALC
CALC
CALC
Prepare configuration and data inputs
1
Automatic BMI module detection from realization file
Supported BMI module config generation
  PET, CFE, Noah-OWP-Modular, t-route
Coming soon
  SoilFreezeThaw, TopModel, LSTM, others

## Slide 13
Weights and BMI model configuration generation are identical for a given spatial domain, hydrofabric version, and realization, meaning these files can often be reused. In addition, forcings can be reused if simulation start and end are static. Recycling these files via the resource directory can be thought of running ngen-datastream in “lite” mode.
*SAVES MONEY*
https://github.com/CIROH-UA/ngen-datastream/tree/main?tab=readme-ov-file#resource_dir-datastream-resources
Hydrofabric
Defines spatial domain
Weights
Indices and coverage used to extract catchment averaged forcings
Forcings
NEXTGEN BMI model configuration
Performs conversion between National Water Model and NextGen forcings formats
Required files for NextGen BMI modules
GET
CALC
CALC
CALC
Prepare configuration and data inputs
1

## Slide 14
ngen-datastream refers to the software chain that builds and validates NEXTGEN input packages (ngen-run/), executes NEXTGEN through NEXTGEN In A Box (NGIAB), and versions the entire run for reproducibility.
Validation
NGEN-DATASTREAM
Prepare configuration and data inputs
1
2
3
Versioning
4
This enforces a standard folder ngen-run/ which makes validation and versioning possible. A standard run folder also allows for other new tools to easily integrate with NGIAB (e.g., DataPreprocessor).

## Slide 15
NEXTGEN Water Modeling Framework Datastream Conceptual Model Breakdown
Realization
Ensures the user has supplied a valid realization file to configure NEXTGEN
Forcings
Required for
Ensures a forcing file exists for each catchment in the hydrofabric and for each time step specified in the realization
BMI configuration
Ensures all BMI model configuration files exist.
The value of the validation step is to notify the user of any errors in the NEXTGEN run package before beginning the execution
Validation
2
Coming soon -> BMI module variable mapping validation

## Slide 16
ngen-datastream refers to the software chain that builds and validates NEXTGEN input packages (ngen-run/), executes NEXTGEN through NEXTGEN In A Box (NGIAB), and versions the entire run for reproducibility.
Validation
NGEN-DATASTREAM
Prepare configuration and data inputs
1
2
3
Versioning
4
This enforces a standard folder ngen-run/ which makes validation and versioning possible. A standard run folder also allows for other new tools to easily integrate with NGIAB (e.g., DataPreprocessor).

## Slide 17
4
Versioning
4
Merkle Tree based hashing algorithm
  “Root” hash allows for quickly identifying if two ngen-run directories are different.
  Ability to query whether some file is a part of the tree represented by the root hash
  Ability to compare files without opening them

## Slide 18
ngen-datastream refers to the software chain that builds and validates NEXTGEN input packages (ngen-run/), executes NEXTGEN through NEXTGEN In A Box (NGIAB), and versions the entire run for reproducibility.
Validation
NGEN-DATASTREAM
Prepare configuration and data inputs
1
2
3
Versioning
4
This enforces a standard folder ngen-run/ which makes validation and versioning possible. A standard run folder also allows for other new tools to easily integrate with NGIAB (e.g., DataPreprocessor).

## Slide 19: customize nextgen simulation resources in aws
ngen-datastream allows users to submit NextGen simulation jobs to cloud-based hosts in Amazon Web Services (AWS)
Users submit jobs via a customizable execution json to a generalizable AWS state machine that manages job execution
Customizable parameters in the execution json include:
Instance Type
Image Id
Number of instances
Volume Size
Region
Security Groups / Instance profile (IAM)
Commands
Terraform allows for quick building of complex AWS infrastructure
Allows users to access HPC resources
Highly configurable execution file allows users to finely tune resources to their ngen executions

## Slide 20: Terraform
Terraform (IaC) builds the AWS state machine
  Build the cloud infrastructure with terraform init, plan, and apply
  Edit the execution json to use an AWS Machine Image built from an ec2 with ngen-datastream installed. Set desired options
  Submit job to AWS state machine via awscli
Takeaways:
  Terraform allows for quick building of complex AWS infrastructure
  Allows users to access HPC resources ($$)
  Highly configurable execution file allows users to finely tune resources to their ngen executions

## Slide 21: Research datastream in aws cloud
  Split VPU daily run - An application of the ngen-datastream AWS state machine
    24-hour CONUS NextGen simulation scheduled each day with AWS EventBridge
    22 individual ec2 instances, 1 for forcingprocessor , 21 simultaneously processing for each VPU
    CONUS runtime determined by the runtime of the largest VPU.

## Slide 22: usage
Be aware of your resources constrains (CPU, Memory, Network)
In general, ngen-datastream memory footprint scales with
  Number of catchments (size of the spatial domain)
  Number of time steps (Simulation duration / output_interval)
If a crash is experienced, either increase the host resources or decrease one or both above dimensions
  Linux commands to monitor resources
    Watch memory usage -> free –h –s2
    Watch processes/cpu usage -> top
    Check available processes -> nprocs
https://github.com/CIROH-UA/ngen-datastream/blob/main/USAGE.md

## Slide 23: options
simulation start and end
NextGen configuration
spatial domain
ngen-datasteam “lite”
AWS s3 mount
RUN options
See the README.md in the repo for an explanation of each variable

## Slide 24: workshop
https://github.com/CIROH-UA/ngen-datastream/blob/main/docs/CIROH_devcon_2024/workshop.md

## Slide 25: Take-aways
ngen-datastream automates the process of collecting and formatting input data for NextGen, orchestrating the NextGen run through NextGen In a Box (NGIAB), and handling outputs. This software allows users to run NextGen in an efficient, relatively painless, and reproducible fashion.
Flexibility in the design allows users to provide their own files if desired.
Scalability via AWS state machine gives users access to HPC resources.
Collaborative process! Feel free to contact me with questions

## Slide 26: Future work
CI/CD
Feedback/Collaboration with community
Realization BMI module variable mapping validation
Expand terraform to include more cloud providers
Expand modules ngen-datastream is aware of
Begin the science!
  Find regional improvements to NextGen realization

## Slide 27: Terms
Catchment – geographic area characterized by a single location, a nexus, where all precipitation in the area runs off through. A drainage basin.
Nexus – the singular point where water flows into or out of a catchment. Often a point along a river.
Subsetting – To reduce a large geopackage (many catchments) down to a smaller geopackage (fewer catchments) . In effect, this is choosing the domain over which ngen will run.
Hashing – SHA256 algorithm applied to files to generate a unique id for a file. Useful for preserving and distinguishing unique inputs.
Validation – Ensuring the ngen input directory data_dir has been constructed properly. Properly meaning that NextGen will not crash and will generate output data.

## Slide 28: Acronyms
NWM – National Water Model
NGIAB – Next Generation National Water Model in a Box
NGEN/NEXTGEN - Next Generation National Water Model
IaC – Infrastructure as code
VPU – Vector Processing Unit
CFE – Conceptual Function Equivalent
PET – Potential Evapotranspiration
NOM – NOAA-OWP-Modular
OWP – Office of water prediction
BMI – Basic Model Interface

## Slide 29: links
ngen-datastream
  https://github.com/CIROH-UA/ngen-datastream/tree/main
Forcingprocessor
  https://github.com/CIROH-UA/ngen-datastream/tree/main/forcingprocessor
Validation
  https://github.com/CIROH-UA/ngen-datastream/blob/main/python/README.md
  https://github.com/NOAA-OWP/ngen-cal
  https://github.com/CIROH-UA/ngen-datastream/blob/main/python/src/datastream/run_validator.py
NextGen BMI module config generation
  https://github.com/CIROH-UA/ngen-datastream/blob/main/python/src/datastream/ngen_configs_gen.py
Hydrofabric Subsetting
  https://github.com/LynkerIntel/hfsubset
Versioning
  https://github.com/makew0rld/merkdir
NGIAB
  https://github.com/CIROH-UA/NGIAB-CloudInfra
ngen-datastream AWS state machine
  https://github.com/CIROH-UA/ngen-datastream/tree/main/terraform
https://docs.ciroh.org/
https://github.com/NOAA-OWP/ngen/wiki
https://ciroh.ua.edu/